# SCAFFOLDING INFORMATION SHEET

Crane erect

- The Scaffolding is to be completed on all sides prior to the start date.

- The Scaffold is to be a minimum 6 board scaffold.

- The inside pole is to be sited from the external frame so as not to interfere with the roofline, with a minimum 2 inside boards and 4 outside boards. Inside board to be no more than 100mm from timber frame.

- The scaffold is to have ALL lifts fully boarded, to include double handrails and toe boards plus ladder access with suitable fixed ladder, to meet current Health & Safety Regulations.

- A minimum of 2 egress routes down the scaffold in line with UKTFA Fire Safety on Timber Frame sites.

- The working lift is to be NO more than 600mm to 700mm below fascia line with no poles interfering with roofline.  Please note if the scaffold does not meet Health & Safety requirements and teams are expected to work in unsafe / unsatisfactory conditions they will be removed from site by ourselves and return at additional cost.

Scaffold Lifts:

All Scaffold lifts are to be installed so that:

a. 	Lifts are to be 600 - 910mm below the top of the ring beam where the lift is adjacent to a floor

b. 	Lifts at soffit level are to be at 910 mm below the top plate, and a minimum of 	600 below the soffit to allow access to the soffit installation team. This may 	mean that, depending on roof pitch and soffit overhang, the top lift may be 	greater than 910mm from the top plate.

- The scaffold must be completed to meet all Health & Safety Requirements and suit our working schedule, or there could be a charge made by Taylor Lane Timber Frame Limited for any delays incurred.

- Scaffold lifts may be subject to change / alteration. Additional lifts or scaffolding may be required on site as design / works progress. At no additional cost to Taylor Lane.

- When our Erectors arrive on site, and before they commence to work on the scaffolding they need to have possession of a copy of the hand-over certificate. Further hand-over certificates must be produced when scaffolding is modified or added to.

COPIES OF THESE MUST BE FAXED TO OUR OFFICES ON

01432 351064.

- Our erectors are instructed never to utilise a scaffold without these certificates as unless these are produced your Public Liability Insurance and our Insurances will be void. The Scaffolding Company will be able to provide you with the certificates and you should request these when ordering the scaffold.

# For further assistance on scaffolding issues please refer to SG28:17 by the National Access and Scaffolding confederation. (Safe system of work for scaffolding associated with Timber Frame Construction).

Please advise scaffolders of overhead power lines, restricted access or shortage of storage space when ordering the scaffold.

No scaffold is to be tied to the timber frame without prior permission of Taylor Lane. Tie loadings must be forwarded along with a report / drawing giving information on types of ties used and their location for approval. Failure to do this will invalidate the structural integrity and line and level of the frame.

Additional costs incurred by the timber frame engineer for such calculations will be forwarded to the client/main contractor. Any additional strengthening required to the frame to aid the stability of the scaffold to be carried out by client/main contractor.

Revised 18th March 2020